## Slide 1
Jal Drishti
Smart Rural Water Quality and Distribution Monitor
Presented by
Group 27
Sampurna Raychaudhuri | Yarragorla Sri Harshitha | Monica M | N Deekshitha | Arushi Katiyar
Mentors
Neha Zanjad | Vishnu Vardhan
WiSH134 | WiSH135 | WiSH136 | WiSH137 | WiSH138

## Slide 2
Empathise
  Sewage contaminated tap water
  Irregular municipal water supply
  Widespread untreated water
consumption
OBSERVED REALITIES

## Slide 3
Defining the problem
The solution must be low-cost, scalable, and easily deployable within existing rural water networks while providing real-time monitoring and alerts.
Water Quality Monitoring
Water Distribution Monitoring
  Difficult to detect pathogen contamination.
  Risk to safe drinking water supply.
  Lack of continuous water quality monitoring.
  Uneven water distribution in rural networks.
  Tail-end households face water shortages.
  Poor distribution affects supply reliability.

## Slide 4
  Lack of real-time water quality monitoring in rural pipelines.
  No early warning mechanism for contamination.
  Unequal water distribution across households.
Transmit data wirelessly to a centralized monitoring platform.
Ideate
Concept Sketches
Final Idea
Feedback
Brainstorm
Challenges
Used feedback for iterative refinement and proactive problem solving
Provide a dashboard or simple mobile/SMS notifications for authorities.
Track flow and pressure data to identify unequal distribution and leakages.
Generate real-time alerts for contamination events.
Use solar-powered IoT devices for autonomous operation.
Monitor parameters such as turbidity, pH, residual chlorine, and flow rate.
Deploy low-cost water quality sensor nodes at source, storage tanks, and distribution points.

## Slide 5
OVERVIEW
GATEWAY NODE
NODE 1
NODE 2
NODE 3

## Slide 6
Water Source
(river)
PROPOSED SOLUTION

## Slide 7
GATEWAY NODE
RASPBERRY PI 4
LORAWAN SX1302
GSM Sim800L
LCD DISPLAY SCREEN
MICROSD CARD
BACKUP BATTERY
GRID POWER
FROM SENSOR NODES
Why did we choose grid power over solar power for RPi?
+5V
+5V

## Slide 8
S
C
H
E
M
A
T
I
C

## Slide 9
Water Source
(river)
FIELD MONITORING NODE 1

## Slide 10
TURBIDITY
FIELD MONITORING NODE 1
ESP 32
SOLAR POWER
TP4056
LiPO BATTERY
BOOST CONVERTER
ORP ELECTRODE
PH PROBE
LORAWAN
24 BIT ADC
Temperature sensor
+5V
SENSOR ARRAY

## Slide 11
S
C
H
E
M
A
T
I
C

## Slide 12
OVERHEAD TANK
Water Source
(river)
FIELD MONITORING NODE 1
FIELD MONITORING NODE 2

## Slide 13
Ph PROBE
LORAWAN SX1286
ORP ELECTRODE
TURBIDITY
24 BIT ADC
Flow sensor
ESP 32
FIELD MONITORING NODE 2
SOLAR POWER
TP4056
LiPO BATTERY
TI BOOST CONVERTER
PRESSURE TRANSMITTER
+5V
Temperature sensor
SENSOR
ARRAY

## Slide 14
OVERHEAD TANK
Water Source
(river)
FIELD MONITORING NODE 1
FIELD MONITORING NODE 2

## Slide 15
ESP 32
LORAWAN SX1286
JUNCTION NODE
SOLAR POWER
TP4056
LiPO BATTERY
BOOST CONVERTER
PRESSURE TRANSMITTER
24 BIT ADC
+5V
Connecting houses with same pressure
SENSOR ARRAY

## Slide 16
S
C
H
E
M
A
T
I
C

## Slide 17
OVERHEAD TANK
Water Source
(river)
FIELD MONITORING NODE 1
FIELD MONITORING NODE 2

## Slide 18
TI COMPONENTS USED
ADS122C04 24-bit ADC
chip module
TI TPS61023 Boost Converter
TI LM35DZ Temperature Sensor
  High 24 bit Resolution Precision
  built-in low-noise PGA
  Achieves up to 94% power
conversion efficiency
  Allows for Ultra-Low Input
Voltage (0.5V)
  Direct Celsius Calibration
  Draws only 60 µA, Minimal Self-Heating

## Slide 19
Core features
Water Quality Diagnostics
  Checks turbidity, pH, chlorine, and E. coli
  Any threshold breach triggers an immediate SMS alert to the operator
Post-Filtration Isolation
  Node1 placed directlly after filtration tank as a critical fail safe
  Catch filtration failures instantly before water reaches storage
Distribution Parity Check
  Track the water volume between OHT node and junction node against a calculated threshold
  Threshold accounts for the exact no of houses connected to a junction
Leakage & Blockage Detection
  Identifies a burst when the flow rate difference between 2 nodes drops by more than 15%
  Detects blockage if water from OHT fails to reach junction node 10 mins
Intermittent Supply
  Monitors Supply Windows
  Can differentiate between non supply window and actual issue
  Saves Power through deep sleep mode during scheduled non supply window
Post-Supply Leakage & Flushing
  Detects zero pipeline pressure
during off hours
  Prevents contaminated water from being sucked into cracks via vacuums
  Executes a 2-minute pipeline flush to
clear next supply cycle
HYBRID ARCHITECTURE
  Integrates distributed end-node hardware with localized edge gateway
  Delivers immediate on-site fail-safe actions alongside a high-level central network
SCALABILITY
  The solution can be expanded to any number of houses
  Thus, the solution is independent of the number of junction nodes and the size of the village

## Slide 20
PROTOTYPE
GATEWAY NODE
NODE 1
NODE 2
NODE 3

## Slide 21
COST ESTIMATION
NODE BASE COST | ₹3000
Water Turbidity Sensor | ₹700
Liquid pH Sensor | ₹900
ORP Sensor | ₹7000
TI LM35DZ Temperature Sensor | ₹250
SUB - TOTAL | ₹11850
NODE BASE COST | ₹3000
QUALITY SENSORS SAME AS NODE 1 | ₹8850
PRESSURE TRANSMITTER | ₹1000
SUB - TOTAL | ₹12850
NODE BASE COST | ₹3000
PRESSURE TRANSMITTER | ₹1000
SUB - TOTAL | ₹4000
NODE 2
TOTAL COST FOR NODES
= ₹(11850+12850+4000)
= ₹28700
  Raspberry Pi 4 (4GB RAM): ₹7,000
  5V 3A AC-to-DC Adapter: ₹600
  LoRaWAN Multi channel SPI Concentrator Shield (SX1302): ₹7,500
  32GB High-Endurance MicroSD Card: ₹1,400
  GSM Sim800L Module: ₹300
  Antenna: ₹300
  3.5 Inch TFT Touch Screen Display: ₹1,150
  Backup battery 20000 mAh battery - ₹1300
TOTAL COST FOR GATEWAY : ₹19550
TOTAL: ₹ (19550 + 28700)
₹ 48250
NODE 1
NODE 3
GATEWAY

## Slide 22
Closed-loop mitigation
Upgrading from open-loop alerts to an autonomous system where RPi controlled solenoid valves instantly isolate contamination lines before distribution
Open data architecture
Streaming real time water quality metrics to a public cloud dashboard to foster municipal oversight and community transparency
Multi-sensor integration
Expanding the sensor array to include Total Dissolved Solids (TDS) and Electrical Conductivity (EC) parameters etc for a more thorough and robust analysis
FUTURE SCOPE

## Slide 23
Decode and extract water quality parameters.
Compare readings against predefined threshold values.
Send SMS notifications via GSM module.
Store historical data on microSD card.
Receive sensor data from multiple LoRaWAN end nodes.
Generate alerts when abnormal conditions are detected.
Update LCD display when requested (Wake-on-Demand)
ORP
pH
Temp
Chlorine,
RASPBERRY PI 4
Provides sufficient processing power for:
  Multi-node data handling
  Threshold analysis
  Alert generation
  Data logging
  Peripheral control (LCD, GSM, microSD)
The SX1302 LoRaWAN concentrator requires a Linux-based operating system for multi node communication.
WHY RPI?
GATEWAY PROCESSING FLOW
.
ORP
Ecoli
Calculates:

## Slide 24
WHY IS IT BETTER TO USE GRID POWER OVER SOLAR POWER FOR THE MAIN GATEWAY?
Unlike an ESP32, RPI consumes 5W in worst case scenario due to the extensive processing and the lack of a deep sleep state.
A grid-powered gateway is more cost-effective over 5 years, costing roughly 61% less than the total investment required for a solar-powered system.
GRID POWER>>>>> SOLAR POWER
For the RPi Gateway

## Slide 25
  Esp32 reads sensors
via LoRa
Why are Esp32s solar powered??
  Esp32 wakes up
Deep sleep
Raspberry Pi
  Deep sleep mode
Active mode: 80-240mA
Deep sleep: 5-150uA
  Asleep for 99%
  power consumption reduced by 95-99%

## Slide 26
CORE NODE BASE COST
  Solar Panel (10W,6V): ₹600
  TP4056 Charging Module: ₹40
  18650 Li-ion Cell: ₹200
  TI TPS61023 Boost Converter: ₹60
  ESP32: ₹300
  LoRa Transceiver (SX1276): ₹400
  IP65 Waterproof Junction Box +
Glands: ₹250
  Antenna- ₹150
  TI ADS122C04 24-bit ADC Chip
Module - ₹1000
SUB-TOTAL: ₹3000/node
  Operating cost: near-zero
  Limited running cost with
1. Minor battery replacement cost 2.Periodic sensor calibration cost
  No manpower/sampling cost
  Low scaling marginal cost because of
shared architecture
JUSTIFIED AS

## Slide 27
1
2
3
5
4
CORE OPERATIONAL CAPABILITIES
WATER QUALITY DIAGNOSTICS
DISTRIBUTION PARITY CHECK
CHECKS TURBIDITY, PH, CHLORINE & E.COLI AT FILTRATION OUTPUT AND OHT END
THRESHOLD BREACH → SMS ALERT TO OPERATOR PROMPTING TO SHUTDOWN OF PUMP/VALVE.
LEAKAGE DETECTION
NON SUPPLY LEAKAGE & FLUSH MANAGEMENT
Flags a main-line burst when ΔQ > 15% of Qnode2 for over 60 seconds
ΔQ=Qnode2 − Qnode3
Alert if ΔQ>0.15×Qnode2
for >60s (filters noise/surges) → SMS MAIN_LINE_BURST with junction location
Tracks supply windows
In-window:
Qnode2>0 & Qnode3=0 for 10 min → BLOCKAGE
Off-window:
Qnode2=0 & Qnode3=0 → no alert, deep sleep mode
Detects prolonged zero-pressure (>2 hrs) during off-hours that risks contaminant ingress at joints/cracks
→ SMS alert +
2 min flush before next cycle
INTERMITTENT SUPPLY MONITORING AND PIPE BLOCKAGE MONITORING
Efficiency Ratio = (Vnode3/Vnode2) × 100, where V = Σ(Q×Δt)
Threshold_min =
100% − [β + (N×α)]
N = houses fed, α = 0.8%/house, β = 5% fixed loss
Ratio < Threshold → SMS alert (unequal distribution)